SHOSHIT  SEVA  SANGH, PATNA - ESTIMATE  OF WORK

The funds would be utilized for the construction of internal roads & pathways, sprucing-up the landscape, construction of the parapet-wall on the roof-top including its plaster and painting. The detailed estimates are below. The above mentioned works need to be completed before the monsoon sets-in by mid/late June. The compound otherwise would be full of slush and in a mess making it possible to keep the school building clean.

(1)Providing & Laying Interlocking Paver Blocks- DSR (20114) ITEM No.16.94 –

Providing and laying factory made chamfered edge Cement Concrete paver blocks of required strength, thickness & size/shape, made by table vibratory method, to attain superior smooth finish using PU or equivalent moulds, laid in required Grey colour & pattern over 50mm thick compacted bed of coarse sand, compacting and proper embedding / laying of inter locking paver blocks into the sand bedding layer through vibratory compaction by using plate vibrator, filling the joints with jamuna sand and cutting of paver blocks as per required size and pattern, finishing and sweeping extra sand in footpath, parks, lawns, drive ways or light traffic parking etc. all complete as per manufacturer’s specifications & direction of Engineer -in-Charge: (a) 80 mm thick c.c. paver block of M-30 grade with approved color design and pattern.

Cost of Work = 37615 Sq.ft=3495.81 Sq.mtr@ Rs. 737.70/ Sq.m =Rs.2578859--(A)

2) Half Brick Work at Parapet (5 ft High) at Roof-

Cost of Work(Market Rate) = 5400 Sq.ft = 501.86@ Rs.850/sq.m=Rs.426579-(B)

3) Cost of Plaster of  Brick Work(DSR ITEM 13.5.1)

= 10800 Sq.ft=1003.71 Sq.mtr@Rs200=Rs.200743------------------------------(C)

4) Cost of  Painting of parapet wall(DSR ITEM 13.45.1)

=1003.71@Rs.146.45=Rs.146993---------------------------------------------------(D)

TOTAL = A+B+C+D= Rs.33,53,174=00